## Slide 1: Verilog Quick Tutorial

## Slide 2
Introduction to CAD Tools

## Slide 3: Need for CAD Tools
We’ve seen basic examples of synthesizing logic expression/equation to logic circuit
    Very simple circuits (10’s of gates)
    Today’s systems consist of millions of gates
Not feasible to manually design these systems

## Slide 4: Number of Choices Available
Most systems designed with help of CAD (Computer-Aided Design) Tools
    Usually packaged into a CAD system to perform tasks such as
    Design Entry, Synthesis, Optimization, Simulation, Physical Design, Verification,
    and so on …
    Many different companies/tools exists today

## Slide 5: Design Flow
Very basic design flow
    Design Entry
    Synthesis and Optimization
    Simulation
    Physical Design

## Slide 6: Design Entry
Design Concept
  What is the circuit supposed to do?
Design Entry
  General structure of how circuit performs desired function
  Typically performed by designer
  Design entry methods
      Truth tables
      Schematic Capture
      Hardware Description Language

## Slide 7: Design Entry with Truth Tables
Design entry using truth tables
    Text file
    Waveform Editor
    Practical only for small designs or sub-circuits

## Slide 8: Design Entry with Schematic Capture
Design entry using schematic capture
  Graphical tool where designer uses mouse to draw circuit diagram
  Library of basic gates designer chooses from
  Designer specifies interconnections
Enables hierarchical design
  Smaller circuits represented by graphical symbol and used in larger circuits
Compared to truth tables, better for larger designs
  Still has limitations

## Slide 9: Design Entry with HDLs
Design entry using HDLs (Hardware Description Language)
  Similar to a computer program
  Describes underlying hardware implementation
Many HDLs exist, two main ones
  Verilog
  VHDL (Very High Speed Integrated Circuit HDL)
Advantages
  Widely supported
  Enables portability
    Underlying implementation can differ without having to change the design specification
  Text-based
    Easy to include in documentation
  Modular implementation possible
    Enables hierarchical implementation of circuits
    Sharing and re-use

## Slide 10: Synthesis and Optimization
Synthesis performed by CAD tool
  Translate design entry into intermediate format
    We assume logic function (for simplicity)
    Realistically intermediate formats vary depending on tool
Likely designer did not optimally specify design
  Logic synthesis or logic optimization performed by synthesis tool
    Important task of manipulating user’s design to produce equivalent, but better circuit
  What makes circuit “better”?
    Size/area, performance, cost, etc …

## Slide 11: Functional Simulation
How do we know our design actually works?
  Functional Simulation
Method
  Designer provides input values
  Functional simulator applies these values to the equations
  Functional simulator produces correspond outputs
    Truth table or timing diagram
  User examines output to verify design
Gate Delay
  Functional simulator assumes delay negligible
  Timing simulator accounts for timing details related to a specific technology

## Slide 12: Physical Design
Physical Design is a type of synthesis
  Sometimes referred to as layout synthesis
  Implement the intermediate format into a technology dependent format
Basys2 FPGA
F = (a+b)’ (cd+a’b) + a’c + bcd

## Slide 13: Expanded Design Flow
Expanded design flow
  Preliminary stages
Designer can use mixture of design entry methods
  Automatically merged into one specification
Iterative process

## Slide 14: C++
C++ as an hardware modeling language is excellent choice for “high-level" behavioral analysis of a system (like evaluating different data flow architectures in a microprocessor).
However C++ lacks the basic hardware concepts like knowledge of strengths, connections, and concurrent execution which complicates model generation for lower level simulations.

## Slide 15: VHDL
VHDL is good for designing Behavioral models
Incorporates some of the modern object oriented techniques.
It's syntax is strange and irregular, and the language is difficult to use.
Structural models require a lot of code that interferes with the readability of the model.

## Slide 16: Why Verilog?
Verilog is a great low level language.
Structural models are easy to design and Behavioral RTL code is pretty good.
The syntax is regular and easy to remember.
It is the fastest HDL language to learn and use.
However Verilog lacks user defined data types and lacks the interface-object separation of the VHDL's entity-architecture model.

## Slide 17
Verilog Programming

## Slide 18: Modules
In Verilog, circuit components are designed inside a module.
Modules can contain both Structural and Behavioral statements.
Structural statements represent circuit components like logic gates, counters, and microprocessors.
Behavioral statements are programming statements that have no direct mapping to circuit components like loops, if-then statements, and stimulus vectors which are used to exercise a circuit.

## Slide 19: Example of Logic module
Lets implement a sample circuit
Module indicates the
start of our specification, end module indicates the end of it
We now have a black box named “example1”
Black box has 4 ports: x1, x2, x3 and f

## Slide 20: Example of Logic module
We now specify which ports are inputs and which one are outputs

## Slide 21: Example of Logic module
If we know the output function directly in terms of inputs we can implement a “behavioral” model of the circuit
/////////////////////////////////
// Module Name: example1
/////////////////////////////////
module example1(x1, x2, x3, f);
input x1, x2, x3;
output f;
assign f = (x1 & x2) + (x3 & ~x2);
endmodule
assign keyword indicates anytime something changes on
right hand side, re-evaluate left hand side

## Slide 22: Major Data Types
Nets
Registers
Parameters

## Slide 23: Nets
Net data type represent physical connections between structural entities.
A net must be driven by a driver, such as a gate or a continuous assignment.
Verilog automatically propagates new values onto a net when the drivers change value.

## Slide 24: Registers
Registers represent abstract storage elements.
A register holds its value until a new value is assigned to it.
Registers are used extensively in behavioral modeling.

## Slide 25: Common mistake in choosing data type
An input port can be driven by a net or a register, but it can only drive a net.

## Slide 26: Common mistake in choosing data type
An output port can be driven by a net or a register, but it can only drive a net.

## Slide 27: Parameters
Parameters are not variables, they are constants.
Typically parameters are used to specify delays and width of variables.

## Slide 28: Types of Modeling
Behavioral
Gate-Level
Structural

## Slide 29: Full Adder Example
module module_name (port_name);
port declarations
datatype declarations
task and function declaration
module functionality and structure
timing specification
endmodule

## Slide 30: Gate Level Verilog Description
xor, and, or are the primitive gate definitions available in Verilog

## Slide 31: Behavioral Level Verilog Description

## Slide 32: Structural Modeling
In structural modeling, you connect components with each other to create a more complex component.

## Slide 33: Structural Modeling
Cin
A
B
Sum
Cout
Sum0
HA
HA
c0
Full Adder
S
c1
module HA (a,b,sum,co);
input a,b;
output sum, co;
assign sum = a^b;
assign co = a & b;
endmodule
module FA (A,B,Cin, Sum,Cout);
input A,B,Cin;
output Sum, Cout;
wire sum0, c0,c1;
HA ha0 (A,B,sum0,c0);
HA ha1 (Cin,sum0,Sum,c1);
assign Cout = co | c1;
endmodule

## Slide 34: Arithmetic Operations

## Slide 35: Bit-Wise Operations

## Slide 36: Logical Operations

## Slide 37: Other Operations

## Slide 38: Unary Operations