## Slide 1: Controllability & Observability

## Slide 2: We learn:
Controllability
Observability

## Slide 3: Controllability and observability
Controllability and observability represent two major concepts of modern control system theory.
These concepts were introduced by R.Kalman in 1960.
Controllability:
In order to be able to do whatever we want with the given dynamic system under control input, the system must be controllable.
Observability:
In order to see what is going on inside the system under observation, the system must be observable.
In a nutshell:

## Slide 4: Controllability and observability formal definition:
Controllability: A system is said to be controllable at time if it is possible to transfer the system from any initial state to any other state in finite interval of time by means of an unconstrained control vector.
Observability: A system is said to be observable at time if it is possible to determine the state of the system from the observation of the output over a finite time interval.
A system is completely controllable if the initial state of the system is transferred to any particular state, in a finite time duration, when a controlled input is provided to it.
Observability of a control system is the ability of the system to determine the internal states of the system by observing the output in a finite time interval when input is provided to the system.

## Slide 5: controllability
Consider the system:
Open-loop system (plant)
state vector
control signal
n×n matrix
B : n×1 matrix

## Slide 6: Controllability:
Is said to be state controllable at if it is possible to construct an unconstrained control signal that will transfer an initial state to any final state in a finite tie interval
If every state is controllable, then the system is said to be completely state controllable.
How to check controllability:
If the system is completely state controllable, then given any initial state x(0), the rank of the n×n matrix CM must be n.
:Controllability matrix
The rank of CM equals the number of linearly independent rows or columns. The rank can be found by finding the highest-order square submatrix that is nonsingular.

## Slide 7: Example 1:
Is the system controllable?

## Slide 8: Solution.
Here determinant of the CM matrix is non-zero.
Also, the rank of CM, n is 2.
So, the system is controllable

## Slide 9: Example 2:
Is the system controllable?

## Slide 10
.
Since the determinant is not zero, the matrix is nonsingular, and the rank of is 3.
We conclude that the system is controllable since the rank of equals the system order.
Ex7.

## Slide 11: Ex8.
Not only is the determinant of this matrix equal to zero, but so is the determinant of any
submatrix. Thus, the rank of is 1.
The system is uncontrollable because the rank of is 1, which is less than the order, 3, of the system.

## Slide 12: Observability:
Consider the unforced system described by the equations
state vector
output vector
A n×n matrix
C : m×n matrix

## Slide 13: observability
The system is said to be completely observable if every state X(t0) can be determined from the observation of y(t) over a finite time interval, . The system is, therefore, completely observable if every transition of the state eventually affects every element of the output vector.
Note: the concept of observability is useful in solving the problem of reconstructing unmeasurable state variables from measurable state variables in the minimum possible length of time.
How to check observability:
the system is said to be completely observable only under the condition that the rank of the matrix OM is n.

## Slide 14: Example 3.
The system is observable or not?

## Slide 15: Solution.
As it is clear that the determinant achieved here is 2, thus is non-zero. Also, the rank here is 2

## Slide 16: Exampel 4.
The system is observable or not?

## Slide 17: Solution:
As it is clear that the determinant achieved here is 1, thus is non-zero. Also, the rank here is 2

## Slide 18: Matlab commands for the computation of controllability and observability matrices.
CONT=ctrb(A,B)
OBSER=obsv(A,C)
The rank of CONT and OBSER respectively determine the controllability and observability of the system.
If rank(CONT) or rank(OBSER) is less than n, where n is the order of the system, the system is not controllable or not observable respectively.
In terms of transfer functions, if the rank(CONT) or rank(OBSER) is less than n, there is a cancellation of terms in the numerator and denominator of the transfer function.
Whether or not the cancellation occurs between the numerator and denominator of the transfer function, we may use the command minreal(sys) to see if we get a simplified transfer function.

## Slide 19: Example 5.
Examine the controllability and observability of the system defined by:
where

## Slide 20
A=[0 1 0;0 0 1;-6 -11 -6];
B=[0;0;1];
C=[5 6 1];
D=0;
CONT=ctrb(A,B)
rank(CONT)
OBSER=obsv(A,C)
rank(OBSER)
CONT =
0 0 1
0 1 -6
1 -6 25
ans =
3
OBSER =
5 6 1
-6 -6 0
0 -6 -6
ans =
2

## Slide 21
This system is controllable, but not observable.
This suggest that there is a cancellation of terms in the numerator and denominator of the transfer function
[num,den]=ss2tf(A,B,C,D)
sys=tf(num,den)
sys=tf(num,den)
num =
0 1 6 5
den =
1.0000 6.0000 11.0000 6.0000
sys =
s^2 + 6 s + 5
----------------------
s^3 + 6 s^2 + 11 s + 6
Continuous-time transfer function.

## Slide 22
pzmap(sys)

## Slide 23
sys_min =
s + 5
-------------
s^2 + 5 s + 6
Continuous-time transfer function.
(s+1) terms in the numerator and denominator of the transfer function are cancelled.
minreal
Minimal realization or pole-zero cancellation
sys_min=minreal(sys)

## Slide 24: Example 6.
Consider the system defined by.

## Slide 25
A=[1 0;0 -1];
B=[1;0];
C=[1 1];
D=0;
CONT=ctrb(A,B)
rank(CONT)
OBSER=obsv(A,C)
rank(OBSER)
[num,den]=ss2tf(A,B,C,D)
sys=tf(num,den)
pzmap(sys)
sys_min=minreal(sys)
CONT =
1 1
0 0
ans =
1
OBSER =
1 1
1 -1
ans =
2
num =
0 1 1
den =
1 0 -1
sys =
s + 1
-------
s^2 - 1
Continuous-time transfer function.
sys_min =
1
-----
s - 1
Continuous-time transfer function.